Switchbank Controller command-response protocol
All command messages must be terminated with a two-byte CRC code followed by ETX {0x03}. All controller response messages are terminated with a two-byte CRC code followed by ETX. Except as a terminating character, and possibly as a byte in the CRC code, ETX may not appear in any message.

Command format details
Messages may contain multiple commands, separated by whitespace (spaces, tabs, new lines, or carriage returns).
[n] indicates that a whole number is expected.
[d] indicates that a decimal number is expected. A whole number is acceptable. Any digits provided beyond the expected precision are ignored. For example, "3", "-4.7", and "134.00" are all acceptable decimal inputs.

Response format details
In controller report templates, '#' represents a numeric digit, '.', a decimal point, '-', a negative symbol. Other template symbols represent characters that may be non-numeric. When a reported number is positive, the negative symbol is replaced with a space, so the message length remains fixed.

Command	Description
r	Request a status report.

Response format template
"## # #####" (10 bytes + "\r\n")

The values represented by the # symbols in the template above are, in sequence:
Channel (the currently selected switch)
State (whether the switch is on (1) or off (0))
Error (sum of active codes from the following list)
0	No error
1	ADC out of range
2	RS232 input buffer overflow
4	RS232 CRC error
8	unrecognized command from RS232
16	invalid device channel
32	datalogging time interval out of range (0..255)

n[n]	Select switch n. [0..63]

0 (zero)	Turn the selected switch off.

1 (one)	Turn the selected switch on.

x	Set all switches off.

h	Show a report header.

Response
"CH S Error" (10 bytes + "\r\n")
z	Show program data.

Response format template
"Aeon Laboratories SB64 V.########-####" (38 bytes + "\r\n")

The # symbols represent the switchbank firmware version.